LAYOUT & SEQUENCE

1. GNX 200 System components

-. 2 Grinding spindles(Coarse grinding and Finish grinding)

Spindle RPM : Max 3600

-. Index table

-. 3 Vacuum chucks (8inch Single Porous Chuck Table)

-. 2 In process gauges

-. 1 Robot

-. Loading/Unloading arm

-. Dry spinner

-. 2 cassette port (8inch Cassette Plate)

-. Vacuum pump unit

2. ITEM & SPECIFICATION

-. GNX200 is capable enough to efficiently process 4",5",6",8" wafer without

troublesome additional modification

-. Down-Feed Grinding

Wafer thickness control can be made by in-situ measuring equipment.

-. Ultimate Accuracy

Air bearing and air cooling mechanism are equipped with the grinding spindle

which is hardly at all affected by thermal variation.

-. Air Bearing

The air bearing consists of carbon graphite.

-. Motorized Spindle Angle Adjustment

Grinding spindle angle can be adjusted by motor.

-. 2 cassette Port

2 cassette port can provide continuous operation after one cassette to another

While one cassette is replaced after process. wafers in the other cassette are ground.

-. THK Variation within one wafer : Less than 1.5um

-. THK Variation between wafers : 2.0um

-. Dimensions(W x D x H) : 1,350 x 2,520 x 1,850

-. Weight : 4.100 Kg